## Slide 1
Priority-Aware Sidelink Resource Allocation
in NR-V2X Networks Using a Double Deep Q-Network
Sunghyun Kim*, Diana Dyussembayeva*, Muhammad Azfar Yaqub**, Dongkyun Kim*
*Kyungpook National University **Free University of Bozen-Bolzano
sunghyunkim@knu.ac.kr, dyussembayevadiana@gmail.com, Muhammadazfar.yaqub@unibz.it, dongkyun@knu.ac.kr
SUMMARY
INTRODUCTION
PROPOSED SCHEME
PROBLEM DEFINITION
CONCLUSION
In NR-V2X sidelink Mode 2, vehicles autonomously select and reserve transmission resources through sensing-based semi-persistent scheduling (SB-SPS). At a dense urban intersection, vehicles detecting the same accident may simultaneously select the same idle subchannel, causing resource collisions. We propose Priority-Aware Double Deep Q-Network (DDQN) resource selection that incorporates message urgency and local resource conditions while retaining SB-SPS sensing and candidate generation. Research-defined weights distinguish CAM, CPM, and DENM traffic and modulate the reward for successful transmission. With 100 vehicles, the proposed method achieves 88% packet delivery ratio (PDR), 44 ms average latency, and 9.5% collision rate. Compared with DQN, this corresponds to an 8-percentage-point PDR gain, 25.4% lower latency, and 36.7% lower collision rate.
NR-V2X V2V Sidelink Mode 2
Vehicles communicate directly through the PC5 interface, including outside network coverage.
Vehicles autonomously select transmission resources from configured or preconfigured sidelink pools.
Fig. 1. NR-V2X sidelink communication in V2V Mode 2.
V2V Messages and Resource Reservation
CPM: sensor-based perception. CAM: periodic vehicle status.
DENM: aperiodic hazard notifications.
SB-SPS senses the preceding 1 s and uses a resource reselection counter (RC) and resource reservation interval (RRI).
Fig. 2. Sidelink subchannel sensing and reservation in Mode 2.
Simultaneous Emergency Resource Selection
Simultaneous selection of an idle subchannel can create duplicate reservations.
Resulting collisions reduce PDR and increase emergency-message latency.
Fig. 3. V2V communication following event detection at an urban intersection.
NS-3 Simulation Settings
Parameter | Value
Area | 500 × 500 m
Vehicles | 20–100
Bandwidth | 20 MHz
Subchannels | 10
Tx power | 20 dBm
Duration | 240 s
Baselines: DQN and
Priority-Aware DQN
Vehicle counts: 20, 40,
60, 80, and 100
Priority-Aware DDQN Resource Selection
Retain SB-SPS sensing and candidate generation.
Message weights: CAM 0.5, CPM 0.7, DENM 1.0
Research-defined QoS policy values, distinct from standardized sl-Priority.
State: sᵢ(t) = [wᵢ, Vᵢ, Qᵢ, Fᵢ]
wᵢ: message priority, Vᵢ: nearby-vehicle density,
Qᵢ: queue state, Fᵢ: future reservations inferred from SCI.
Action: aᵢ(t) ∈ {1, 2, …, Kᵢ}
Reward: Rᵢ(t) = λₛ(1 + αwᵢ)Sᵢ(t)
DDQN separates online action selection from target-value evaluation. Message urgency scales the success reward.
Fig. 4. PDR
PDR at 100 vehicles
88%
8 percentage
points higher
than DQN
DQN: 80%
Priority-Aware DQN: 84%
Fig. 5. Latency
Average at 100 vehicles
44 ms
25.4% lower
than DQN
DQN: 59 ms
Priority-Aware DQN: 52 ms
Fig. 6. Collision rate
Rate at 100 vehicles
9.5%
36.7% lower
than DQN
DQN: 15.0%
Priority-Aware DQN: 12.5%
Priority-Aware DDQN incorporates message urgency and local resource conditions while retaining SB-SPS sensing and candidate generation. The method improves PDR and lowers latency and collision rate under the evaluated conditions. Relative to Priority-Aware DQN at 100 vehicles, latency and collision rate decrease by 15.4% and 24.0%, respectively.
Future Work
Evaluate simultaneous DENM bursts in a standards-based NR-V2X PHY/MAC environment. Measure message-specific PDR, latency distributions, and delivery probability within the deadline.
Notes: Source: ICCT2026_English(1).docx. Sections I, III, IV, and V; original Figs. 1–6; Eqs. (2), (3), (5), and (7); Table I.